## Slide 1
Autonomous Guidance for Asteroid Descent using Successive Convex Optimisation
Dual Quaternion Approach
Dr. ir. E. Mooij | TU Delft, Astrodynamics and Space Missions
Dr. ir. M. Sagliano | Deutsches Zentrum fur Luft-und Raumfahrt e.V.
S. Hazra

## Slide 2: Why asteroids?
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
Notes: Asteroids are pristine remnants from the planetary formation. The study of their composition can help understand the process better. They are plentiful in resources and stand as an option for mining.
Chelyabinsk impact, 20 m dia asteroid, shockwave across six cities. The threat of impact with Earth, requires missions like asteroid redirect mission. They are therefore a hot topic at present.

## Slide 3: Recent Missions
OSIRIS-REx
Hayabusa 2
Rosetta
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
Notes: The most current missions to asteroids that have either conducted sampling missions or close proximity operations to small bodies are: . The current phases of these missions are as follows.
For this thesis we take inspiration from Osiris Rex and Rosetta, since we would like to present a solution for a sampling mission for MAB asteroids. (These are between Mars and Jupiter and also less weathered due to their further positioning from the sun as compared NEAs).

## Slide 4: Why dual quaternions (DQs)?
General 6DOF representation
  Position: Cartesian coordinates
  Attitude: Quaternion
Dual Quaternion 6DOF representation
  Position: Quaternion
  Attitude: Quaternion
Advantages of dual quaternions
  One transformation for both rotation and translation
  Compact representation of 6DOF kinematics and dynamics
  Similar properties as quaternions
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
Notes: Others available for attitude: Euler rotation, MRPs
Dual quaternions: 8 tuple representation, one transformation for both rotation and translation

## Slide 5: Why autonomous guidance?
A priori information about asteroids is limited
Perturbed and variable environment
Shapes, rotation rates and densities might be irregular or variable
Distance from Earth around 1.1-2 au
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
Notes: 1. shape, size, rotation rates, densities etc
2. Highly perturbed, Non central gravity field – SRP – 3BP– stable orbits can turn to crashing or escape orbits (seen in mission also Philae)
3. fast rotation – dynamics unpredictable
4. MAB – 2.1 to 3 au, communication ~17 to 33 mins, remote operation costly, delay in comm in unforeseen circumstances (The further we go from the sun, the sampled material becomes more and more primitive. )
5. Restrictions on SC design for fuel requirements

## Slide 6: What are the available guidance technologies?
Pseudospectral Methods
Artificial Potential Functions
Convex Optimisation
Sampling Based Motion Planning
Selected Autonomous Guidance Technologies
  Successive Convex Optimisation
  Sampling Based Model Predictive Optimisation
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
Notes: 1. shape, size, rotation rates, densities etc
2. Highly perturbed, Non central gravity field – SRP – 3BP– stable orbits can turn to crashing or escape orbits (seen in mission also Philae)
3. fast rotation – dynamics unpredictable
4. MAB – 2.1 to 3 au, communication ~17 to 33 mins, remote operation costly, delay in comm in unforeseen circumstances (The further we go from the sun, the sampled material becomes more and more primitive. )
5. Restrictions on SC design for fuel requirements

## Slide 7: How can a spacecraft autonomously descend for a touch-and-go sampling process to a chosen landmark robustly and optimally, while being accurate and safe?
How can the SC attitude and orbital dynamics be represented by dual quaternions?
What are the cost functions that need to be optimised, the constraints they are subject to and how can they be formulated with dual quaternions?
How can the method of successive convex optimisation (SCvx) be implemented to optimise the derived cost functions?
What methods can be used to verify and validate the subsystems and guidance algorithm to qualify the system to be accurate, safe and robust?
How useful is this representation and can it be used in real time autonomous applications?
How can the method of sampling based model predictive optimisation (SBMPO) be used to map a small Solar System body autonomously to provide the SC with a safe landmark for descent?
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 8: Which small Solar System bodies?
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
Requirements
  Sufficient property models available
  Irregularly shaped and varied sizes
Table 1: Key Parameters of Target Small Solar System Bodies
Figure 1: Kleopatra (Top left), Comet 67P (Top right) and Itokawa (Bottom). (Not to scale)

## Slide 9: Which spacecrafts (SCs)?
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
Requirements
  Able to operate at a distance of 1.2~3 au from the Sun
  Able to conduct descent on a small Solar System body
Table 2: Specifications of Rosetta and OSIRIS-Rex as reference SCs for mapping and descent
Figure 2: OSIRIS-REx (Top), Rosetta (Bottom). (Not to scale)

## Slide 10: What is the environment like?
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
Internal disturbances
  Flexible dynamics
  Sloshing
External disturbances
  Perturbed gravity
  Solar Radiation Pressure
  Third Body Perturbation
Figure 3: Gravitational and perturbing accelerations on Rosetta, while performing close proximity operations at Comet 67P.

## Slide 11: What is required from the guidance algorithm?
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
Minimum propellant consumption
Constrained SC altitude
Constrained SC attitude
Constrained SC angular rate
Constrained SC thrust
Optimal descent trajectory
Optimal mapping trajectories

## Slide 12
General 6DOF representation:
SC State Vectors
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
DQ 6DOF representation:

## Slide 13
General 6DOF representation:
SC kinematics and dynamics in the asteroid rotating frame of reference (A)
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
DQ 6DOF representation:
    Translational and Rotational Kinematics:
    Translational and Rotational Dynamics:
    Translational and Rotational Kinematics:
    Translational and Rotational Dynamics:

## Slide 14
Convex optimisation benefits over other techniques
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
General optimal control problem:
Objective/Cost function
Inequality constraints
Equality constraints
The cost function, inequality and equality constraints can be linear or non-linear.
An asteroid descent problem is ridden with such non-linearities.
Convex optimisation, though being a young development has proved to be very beneficial for such non-linear optimal control problems

## Slide 15
Lossless Convex Optimisation
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 16
Successive Convex Optimisation
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 17
Dynamic Successive Convex Optimisation
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 18
Sampling Based Model Predictive Optimisation
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 19
Simulator Architecture
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification
Figure 3: Simulator Architecture for Descent Guidance

## Slide 20
Asteroid Models
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 21
SC models
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 22
Environmental Models
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 23
DQ Kinematics and Dynamics
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 24
Dynamic Successive Convex Optimisation (Mars 6DOF)
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 25
Dynamic Successive Convex Optimisation (Mars 6DOF DQs)
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 26
Scenario 1
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 27
Scenario 2
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 28
DQ Scenario 1 and 2
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 29
Asteroid Mapping Initialisation
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 30
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 31
Research Question
Introduction
Mission Overview
Methodology
Results
Conclusions
Recommendations
Simulator Verification

## Slide 32: References
https://www.space.com/30213-asteroid-mining-planetary-resources-2025.html
https://www.nasa.gov/content/what-is-nasa-s-asteroid-redirect-mission
https://www.asteroidmission.org/?latest-news=nasa-mission-reveals-asteroid-big-surprises
https://www.extremetech.com/extreme/286238-hayabusa-2-successfully-collects-sample-from-asteroid-ryugu

## Slide 33: Questions?
Thank You!